## Slide 1
AI-Enhanced BGP
Autonomous Control Plane
Final Project Review
Sudalai Kumar M — 2024503703
Ajay Kumar S — 2024503701
Satlas Rohit B — 2024503305
Srinivasan S — 2024503707
AS 65001
Transit
AS 65003
Regional
AS 65004
Regional
AS 65007
Stub
AS 65008
Stub
AS 65009
Stub

## Slide 2
Problem Statement and Motivation
AI-Enhanced BGP Autonomous Control Plane | 02
• BGP route advertisements are exchanged between autonomous systems; a wrong or leaked route can redirect traffic or distort path selection.
• The project targets observable symptoms: origin-AS mismatch, suspicious sub-prefixes, route churn, long/changed AS paths, and valley-free violations.
• A detector alone is insufficient: mitigation must change the local policy and the resulting routing state must be checked.
• Implemented scope is a controlled FRRouting testbed with synthetic attacks and topology-local replays of selected historical incidents.
Observe
Route + AS path + recent history
Assess
ML class + behavioural trust
Act and verify
FRR policy + RIB checks
Engineering objective: close the loop, not just raise an alert.

## Slide 3
Project Objectives and Scope
AI-Enhanced BGP Autonomous Control Plane | 03
• Collect route and peer state from FRRouting and preserve time-ordered observations.
• Convert each route observation into a fixed 10-feature behavioural vector.
• Combine calibrated model output with explicit behavioural indicators and weighted trust.
• Map decisions to local policy actions; use shadow validation and route-state checks in the full A4 variant.
• Evaluate six configured scenarios, model quality, false actions, ablations and repeated trials.
Testbed
FRRouting 10.2.1 in Docker-based environment
Scenarios
S1–S6: hijack, sub-prefix, flapping, replayed incidents
Experiment variants
A0–A4: baseline → heuristics → ML → trust → full system
Evidence boundary
Lab/testbed experiments; not Internet-wide deployment
Scope is limited to the configured topology, observation vantage point, data and tested scenarios.

## Slide 4
BGP Fundamentals and Threat Model
AI-Enhanced BGP Autonomous Control Plane | 04
What the controller reasons about
• Prefix: the destination network being advertised (for example, 192.0.2.0/24).
• AS path: ordered AS sequence carried with a route advertisement.
• Origin change and longer/more-specific prefixes are used as behavioural signals.
• Local Preference is a local policy attribute used to influence route choice.
AS 65007
Legitimate origin
AS 65010
Rogue origin in test
AS 65003
Observation / decision point
Threat cases configured: direct prefix hijack, /25 sub-prefix hijack, route-flapping burst, and route-leak patterns.
Important: the project observes selected routes at a local vantage point; it does not have global visibility into every BGP path.

## Slide 5
Existing Approach and Proposed System
AI-Enhanced BGP Autonomous Control Plane | 05
Reference approaches
• Standard BGP: route selection without this project's detector or autonomous mitigation.
• Deterministic rules: interpretable checks on origin, prefix length, path and churn.
• RPKI-ROV baseline is represented in the comparative evaluator, but the tested route-leak cases are marked out of scope for origin validation.
Implemented A0–A4 progression
A0
Standard BGP
A1
BGP + Heuristics
A2
BGP + ML only
A3
ML + behavioural trust
A4
ML + trust + shadow validation
Evaluation does not establish that ML is universally better: offline LR and the heuristic result match on the reported aggregate metrics.

## Slide 6
System Architecture
AI-Enhanced BGP Autonomous Control Plane | 06
FRRouting
BGP peers / routes
Telemetry collector
FRR CLI / JSON
History store
SQLite + JSONL
Feature extractor
10 features
Classifier + trust
Class, probability, score
Decision engine
Reasons + class ID
Shadow validator
Stage / accept / reject
Policy engine
LocalPref / community
RIB verification
Expected route state
Rollback / recovery
Restore prior policy on failure
Asynchronous control loops coordinate telemetry, inference, policy action, heartbeat and system metrics.

## Slide 7
Network Topology and Experimental Environment
AI-Enhanced BGP Autonomous Control Plane | 07
AS 65001
Transit core
AS 65002
Transit core
AS 65003
Regional
AS 65004
Regional
AS 65005
Regional
AS 65006
Regional
AS 65007
Stub
AS 65008
Stub
AS 65009
Stub
AS 65010
Rogue test AS
10 configured ASes
Docker / FRR 10.2.1
Python 3.13.5
Windows 11 test environment
Topology is a controlled lab; historical incidents are topology-local replays, not live Internet incidents.

## Slide 8
Telemetry Collection and Feature Engineering
AI-Enhanced BGP Autonomous Control Plane | 08
FRR snapshot
Prefix, next hop, AS path, origin, LocalPref, peers
Route history
Timestamped transitions (last 60 s / 5 min)
Feature extractor
Baseline comparison + relationship checks
10-value feature vector
Model input with fixed schema
Path
as_path_len • as_path_edit_distance
Origin / prefix
origin_as_change • prefix_mask_len
Churn
announcements_per_minute • flap_count_5min
Policy / age
loc_pref_current • route_age_seconds
Relationship / peers
valley_free_violation • neighbor_diversity
Storage: SQLite tables for route events, peers, system metrics and convergence events; JSONL append log for route events.

## Slide 9
Machine-Learning and Trust Assessment
AI-Enhanced BGP Autonomous Control Plane | 09
10 features
Scaled by saved scaler
Classifier
Random Forest or Logistic Regression
4-way output
Normal / Suspicious / Leak / Hijack candidate
Trust score
Weighted behavioural score
Trust weights implemented in hybrid_engine.py
Origin stability
20%
Path adherence
20%
Flap quiescence
15%
Prefix legitimacy
15%
Peer consistency
10%
ML normal probability
20%
Offline test (109 samples): Random Forest accuracy 81.65%, macro-F1 0.4117; Logistic Regression accuracy 83.49%, macro-F1 0.4283. Both models miss all Suspicious (4) and Route Leak Candidate (7) test examples.
Model metrics are aggregate offline results; minority-class recall is the key limitation.

## Slide 10
Anomaly Detection and Decision Logic
AI-Enhanced BGP Autonomous Control Plane | 10
Signals that generate diagnostic reasons
Origin mismatch
origin_as_change > 0.5
Sub-prefix
prefix mask length > /24
Route churn
flap_count_5min ≥ 3
Path anomaly
valley-free violation or edit distance ≥ 2
These reason tags explain the route context; classification ID comes from the selected model's argmax probability.
Illustrative example — not an observed trial
Baseline origin 65007; observed origin 65010
Feature
origin_as_change = 1; prefix/path context retained
Assessment
ML class + weighted trust score + reason tags
Policy mapping
Class and trust determine LocalPref / community

## Slide 11
Policy Generation and Autonomous Mitigation
AI-Enhanced BGP Autonomous Control Plane | 11
Configured policy response tiers
Normal
LocalPref 100
No mitigation
Suspicious
LocalPref 80
Soft deprioritisation
Route-leak candidate
LocalPref 50
Hard deprioritisation
Prefix-hijack candidate
LocalPref 0 + no-export
Quarantine / suppress export
Action sequence
1. Decision engine emits class, confidence, trust and reasons
2. Policy engine maps the route to LocalPref / community
3. FRR configuration is applied through vtysh
4. Return status is not the same as desired RIB state
Mitigation is a routing-policy change at the observing router; it does not globally remove an advertisement from the Internet.

## Slide 12
Safety, Verification and Rollback
AI-Enhanced BGP Autonomous Control Plane | 12
Observe
Capture route + history
Assess
Class / trust / reason
Validate
Shadow-stage candidate
Apply
Write FRR policy
Verify
Check route / RIB state
Monitor
Track sustained state
Recover
Rollback if verification fails
Why verification matters
• A successful CLI call only proves command acceptance.
• The controller must compare observed RIB state with expected policy outcome.
Recovery behaviour
• Previous policy/state can be restored by rollback support.
• Test files cover shadow rejection, rollback and RIB verification; tests are not proof of Internet-scale resilience.

## Slide 13
Experimental Setup and Results
AI-Enhanced BGP Autonomous Control Plane | 13
Full-system A4: 20 trials per scenario
ID | Scenario | Detect rate | Mitigation success
S1 | Direct prefix hijack | 95% | 95%
S2 | Sub-prefix /25 hijack | 100% | 100%
S3 | Route-flapping burst | 0% | 0%
S4 | YouTube 2008 replay | 100% | 100%
S5 | Google 2017 route leak | 0% | 0%
S6 | Cloudflare 2019 route leak | 0% | 0%
Normal-traffic stress test
1,000 attack-free windows
RF standalone: 3.2% false actions
Full A4: 3.2% false-action rate
Heuristics: 75% false alarms
Offline model test (109 samples)
LR: 83.49% accuracy; macro-F1 0.4283
RF: 81.65% accuracy; macro-F1 0.4117
Interpretation: success depends strongly on scenario visibility and route selection. Three scenario classes show no detections in the 20-trial table. The attack-free stress test still records false mitigation actions.
MTTD/MTTM are reported only where detections occurred; N/A reflects no detection, not zero latency.

## Slide 14
Limitations and Future Work
AI-Enhanced BGP Autonomous Control Plane | 14
Demonstrated limitations
• Offline minority-class performance is poor: the reported RF and LR models miss all Suspicious and Route Leak Candidate test examples.
• Full A4 detects none of the tested route-flapping burst or route-leak replay trials.
• Failure analysis attributes many outcomes to observability / non-best-path selection at the monitoring vantage point.
• False actions remain in attack-free traffic under the full-system stress test.
Practical next steps
• Expand telemetry beyond the selected best path where the platform allows it.
• Improve minority-class labels, sample balance and evaluation methodology.
• Test across more topologies and policy configurations, including route-leak visibility.
• Tune staged actions against false-positive cost; keep post-action RIB checks and rollback.
These are proposed improvements, not completed capabilities.

## Slide 15
Conclusion
The project integrates BGP telemetry, route-history features, model-based classification, behavioural trust and policy action in an FRRouting testbed.
The experiments demonstrate useful responses for selected hijack scenarios—but also expose missed route leaks, missed flapping and false actions. Verification and rollback are therefore central to further development.
Questions & Discussion
Observe
BGP state
Act
Policy + verification
Assess
Trust + class